## Slide 1
AMIRIS Germany 2027
Where we are, and why the current result is likely close to the ceiling
Muideen Oladayo Ajiboye | 29 September 2026
Supervisor meeting before travelling to Nigeria - thesis to continue virtually from there

## Slide 2
What This Thesis Is Testing
• AMIRIS: an open, agent-based electricity market simulator (DLR) - each power plant, storage unit and demand type is modelled as its own decision-making agent
• Energy Brainpool: a commercial forecasting firm - their real 2027 hourly price forecast for Germany is the benchmark
• The question: can a research-grade, open simulation tool built from real public data get close to a commercial forecaster's result?
• Everything shown today is built from Brainpool's own real 2027 input data, or independently-sourced real data (ENTSO-E, Eurostat, BNetzA, DWD) - nothing is invented to make numbers agree
AMIRIS Germany2027 | Supervisor Meeting | 2

## Slide 3
Where We Started vs. Where We Are
3-7x too high
First comparison (early build)
within ~1 EUR/MWh
Current best build (Phase 37)
7 of 8,760 hours
Still hard to match exactly
• The first honest comparison against Brainpool's real price looked alarming: AMIRIS came out 3-7x too expensive on average
• That gap was diagnosed, not assumed - traced to how the import model handled cross-border electricity, then fixed and calibrated
• After many rounds of real, data-grounded refinement (52 documented phases), AMIRIS's average price is now almost identical to Brainpool's
• What remains: 7 unusual hours out of the whole year where AMIRIS still shows a price spike Brainpool's forecast never shows
AMIRIS Germany2027 | Supervisor Meeting | 3

## Slide 4
Current Best Result (Phase 37)
This is the build the thesis is written around
Metric | AMIRIS (Phase 37) | Brainpool's real forecast
Average price (whole year) | 67.45 EUR/MWh | 68.04 EUR/MWh
Hours with a physical shortage | 7 (0.08% of the year) | 0
Average error, ordinary hours | -2.90 EUR/MWh | reference
Pattern-matching (correlation), ordinary hours | 0.72 | reference
• “Ordinary hours” = the 99.92% of the year with no extreme shortage event - the fair, trustworthy comparison
• On those hours, AMIRIS's average price sits under 3 EUR/MWh from Brainpool's, and the two track each other reasonably well hour to hour
• The honest remaining gap is entirely concentrated in 7 specific hours - not a general accuracy problem
AMIRIS Germany2027 | Supervisor Meeting | 4

## Slide 5
“Why Doesn't AMIRIS Just Import Instead of Hitting 3,000 EUR/MWh?”
Group A - 4 of the 7 hours: the cable is completely full
Import already sits at 22,011.8 of a real 22,012 MW transmission limit (built from real 2023 cross-border flow data, not a placeholder). It is not that import is expensive - physically, no more electricity can flow down that connection at any price. This is a real, hard limit, correctly represented.
Group B - the other 3 hours (all one evening, 17 Dec): the cable has room to spare
Import sits well BELOW the limit (19,700-21,200 of 22,012 MW) - real spare capacity going unused. Rest-of-Europe's storage is sitting on 655,000+ MWh of stored energy and faces a huge price gap (Germany near 3,000 EUR/MWh vs. its own market near 163) - yet it discharges ZERO. It is not choosing not to help because it is too expensive; its own forecaster simply never sees Germany's price at all when deciding whether to discharge.
• Direct answer: import cost is not the reason in either case - one is a physical capacity limit, the other is an information gap in the model
AMIRIS Germany2027 | Supervisor Meeting | 5

## Slide 6
What We Tried to Close the Remaining Gap
Real experiments - reporting the negative results honestly, not hiding them
• 3 alternative weather/demand years for renewables and demand - no improvement (Phases 49-51)
• A negative price floor, as the supervisor suggested - confirmed dead end (Phase 29)
• A real plant start-up cost - the mechanism turned out not to be wired into AMIRIS's dispatch logic at all (Phase 30)
• Widening how far generators can bid from their true cost - made pattern-matching worse, not better (Phases 31, 47)
• Splitting the single “Rest of Europe” zone into 10 real separate countries, then a full real transmission mesh - more complex, not more accurate (Phases 42-43, 48)
• Recalibrating the import capacity ceiling - a real trade-off in both directions, no clean win (Phases 25-27)
AMIRIS Germany2027 | Supervisor Meeting | 6

## Slide 7
One Thing That Did Move the Needle (Investigative Only)
• Opened AMIRIS's own Java source code directly and found exactly why Rest-of-Europe's storage “can't see” Germany's shortage price
• Patched it: storage now gets a boosted incentive when Germany's price is genuinely higher than its own
• Best version found: shortage hours 7 → 6, average error -2.90 → -0.95 EUR/MWh
• But: pattern-matching and average hour-to-hour error both got slightly worse - a genuine trade-off, not a clean win
• Why: Rest-of-Europe's storage only has so much energy it can move in one day - helping the morning leaves less for the evening peak the same day
Reported to the department as a technical finding - not adopted into the thesis.
Exactly as agreed: an investigative side-experiment, kept in its own separate, fully-documented build, with the thesis's actual result (Phase 37) left untouched.
AMIRIS Germany2027 | Supervisor Meeting | 7

## Slide 8
Why Phase 37 Is Likely Close to the Best Achievable Result
• 52 documented phases of real, data-grounded experiments - every lever AMIRIS actually exposes has now been tested
• The remaining gap has two different, structural causes: a real physical transmission limit (Group A), and a genuine architectural limit in how each zone's forecaster works (Group B)
• Even directly patching the one fixable cause (Phase 52) only trades one problem for another - Rest-of-Europe's storage has a hard daily energy budget that more code cannot create out of thin air
• Brainpool's own real forecast never exceeds 330 EUR/MWh all year - their model never represents this kind of extreme scarcity event either, so the two models are not really answering the exact same question at the extreme tail
Conclusion
Further tuning is very unlikely to beat Phase 37 by any meaningful margin. The sensible next step is to finalise the write-up with Phase 37 as the reference result, and report the remaining 7-hour gap as a well-understood, structural limitation rather than an unresolved bug.
AMIRIS Germany2027 | Supervisor Meeting | 8

## Slide 9
Continuing Virtually From Nigeria
• All work is tracked in git - every phase, every result, every dead end is already committed and reproducible
• The build environment, scripts, and full Progress Report travel with me - no work is tied to being on campus
• Will continue the thesis write-up remotely and can share updates the same way as this meeting
• Available for a follow-up call or written check-in at a time that works for both of us
AMIRIS Germany2027 | Supervisor Meeting | 10

## Slide 10
Thank you - questions and discussion